## Slide 1: CSC 101 – Introduction to Computing
Lecture 3-4

## Slide 2: Outline
Memory
Memory Hierarchy
Storage Devices:
  Magnetic Storage Devices
  Optical Storage Devices
  Solid State Storage Devices
  Data Read & Write Process.

## Slide 3: Memory
Memory
  Refers to chip-based storage located inside the system unit
  Storage refers to the amount of long-term storage
available to a computer
  Random Access Memory (RAM)
    Computer’s main memory
    Consists of chips arranged on a circuit board called a memory module which are plugged into the motherboard
    Stores essential parts of operating system, programs, and data the computer is currently using

## Slide 4: Memory

## Slide 5: Memory
Volatile
  RAM content lost when the computer is shut off
  ROM and flash memory are non-volatile
Measured in bytes
  Amount installed depends on the CPU and operating system being used
Most personal computers use SD-RAM
MRAM and PRAM - non-volatile RAM under development

## Slide 6: Memory
Each location in memory has an address
  Each location typically holds one byte
  Computer system sets up and maintains directory tables to facilitate retrieval of the data

## Slide 7: Memory
Registers
  High-speed memory built into the CPU
  Used to store data and intermediary results during
processing
  Fastest type of memory
ROM (read-only memory)
  Non-volatile chips located on the motherboard into which data or programs have been permanently stored
  Retrieved by the computer when needed
  Being replaced with flash memory

## Slide 8: Memory
Flash Memory
  Nonvolatile memory chips that can be used for storage
  Have begun to replace ROM for storing system
information
  Now stores firmware for personal computers and other devices
  Built into many types of devices (media tablets, mobile phones, and digital cameras) for user storage

## Slide 9: Memory Hierarchy

## Slide 10: Storage System Characteristics
Storage Media and Storage Devices
  Medium
    Hardware where data is stored
    DVD disc, flash memory card, etc.
  Device
    DVD drive, flash memory card reader, etc.
    Medium is inserted into device to be used
  Can be internal, external, or remote
  Storage devices are typically identified by letter

## Slide 11: Storage System Characteristics
Volatility
  Storage media are nonvolatile
Random vs. Sequential Access
  Random access (direct access) allows data to be retrieved from any location on the storage medium
  Virtually all storage devices use random access
  Sequential access means retrieval of data can occur only in the order in which it was physically stored on the storage medium
    Magnetic tape drive

## Slide 12: Storage System Characteristics
Logical vs. Physical Representation
  File
    Anything stored on a storage medium, such as a
program, document, digital image, or song
  Filename
    Name given to a file by the user
  Folder
    Named place on a storage medium into which files can be stored

## Slide 13: Storage System Characteristics

## Slide 14: Storage System Characteristics
Logical file representation
  Individuals view a document stored as one complete unit in a particular folder on a particular drive
Physical file representation
  Computers access a particular document stored on a storage medium using its physical location or locations
Types of Storage Technology Used
  Magnetic (conventional hard drives)
  Optical (optical discs)
  Electrons (flash memory media)

## Slide 15: Hard Drives

## Slide 16: Hard Drives
Hard disks are divided into:
  Tracks
    Concentric path on disk where data is recorded
  Sectors
    A small piece of the track
  Clusters
    One or more sectors; smallest addressable area of a disk
  Cylinders
    Collection of tracks located in the same location on a set of hard disk surfaces

## Slide 17: Hard Drives

## Slide 18: Hard Drives
Solid State Drives (SSDs)
  Use flash memory technology
  Use less power and have no moving parts
  Particularly appropriate for portable computers and mobile devices

## Slide 19: Internal and External Hard Drives

## Slide 20: Hard Drive Speed, Disk Caching, and Hybrid Hard Drives
Disk access time
  Total time that it takes for a hard drive to read or write data
  Consists of seek time, rotational delay, and data movement time
    SSDs don’t require seek time or rotational delays
Disk cache
  Memory used in conjunction with a magnetic hard drive to improve system performance
  Typically consist of memory chips on a circuit board inside the hard drive case

## Slide 21: Hard Drive Speed, Disk Caching, and Hybrid Hard Drives
Hybrid Hard Drive
  Combination of flash memory and magnetic hard drive
  Uses flash memory for cache
  Allows encryption to be built into the drive

## Slide 22: Optical Discs and Drives
Optical Disc Characteristics
  A type of storage read from and written to using laser beams
  Today’s standard for software delivery
  Divided into sectors like magnetic discs but use a single spiral track (groove)
  Have a relatively large capacity and are durable
  Used for backup purposes and for storing and transporting music, photos, video, etc.

## Slide 23: Optical Discs and Drives
Representing Data on an Optical Disc
  Read-only optical disc
    Surface of disc is molded or stamped
  Recordable or rewritable disc
    Optical drive is used and the reflectivity of the disc is changed using a laser to represent the data
  Pits and lands are used to represent 1s and 0s
  The transition between a pit and a land represents a 1; no transition represents a 0

## Slide 24: Optical Discs and Drives

## Slide 25: Optical Discs and Drives
Optical Drives
  Three categories of discs: CD, DVD, or Blu-Ray Disc (BD)
  Can be read-only, recordable, or rewritable
  Almost always downward compatible
  Can support single or dual layer discs
  Recording data onto disc is called burning
  Can be internal or external drives
    External drives typically connect via USB port

## Slide 26: Optical Discs and Drives
Optical Disc Shapes, Sizes, and Capacities
  Standard size is 120-mm (about 4.7 inches)
    Mini discs are smaller—80-mm
  Theoretically can be made into various shapes—hearts, triangles, irregular shapes, or a hockey-rink shape
    Patent battle exists about changing optical disc shapes
    None of these different shapes are currently available

## Slide 27: Optical Discs and Drives

## Slide 28: Flash Memory Storage Systems
Flash Memory
  Chip-based storage medium that represents data using electrons
  Used in SSDs and hybrid hard drives
Embedded Flash Memory
  Flash memory chips embedded into products, such as
    Portable digital media players, digital cameras
    Handheld gaming devices, GPS devices, mobile phones
    Sunglasses and wristwatches

## Slide 29: Flash Memory Storage Systems

## Slide 30: Flash Memory Storage Systems

## Slide 31: Flash Memory Storage Systems
USB Flash Drives
  Sometimes called flash memory drives, jump drives, or thumb drives
  Flash memory media integrated into a self-contained unit that plug into and is powered by a USB port
  Designed to be very small and very portable
  Available in a host of formats including custom shapes
  Can be built into a consumer product
  Can be used to lock a computer and to issue Web site passwords
  Can include biometric features, such as a built-in fingerprint reader

## Slide 32: Flash Drive Storage Systems

## Slide 33: Other Types of Storage Systems
Network Storage and Cloud Storage Systems
  Remote storage
    Using a storage device not directly connected to the
computer being used
    Accessed through the Internet or through a network
  Network storage
    Remote storage via local network

## Slide 34: Network and Cloud Storage Systems
Network attached storage (NAS)
  High performance storage systems connected individually to a network
  Designed for small business and home use
Storage area network (SAN)
  Separate network of hard drives or other storage devices
which are attached to the main network

## Slide 35: Network and Cloud Storage Systems

## Slide 36: Network and Cloud Storage Systems
Cloud storage (online storage)
  Accessed via the Internet
    Via Web sites (Flickr, Facebook, Google Docs, etc.)
    Via online storage sites (Box, Dropbox, etc.)
    Growing in importance because more and more applications are Web based
    Increasing being used for backup purposes
    Files can be synched between PC and cloud storage
    Many Web sites providing online storage offer it free
    Business cloud storage is available

## Slide 37: Network and Cloud Storage Systems

## Slide 38: Smart Cards
Smart Card
  Credit card-sized piece of plastic that contains some computer circuitry (processor, memory, and storage)
  Stores small amount of data (about 64 KB or less)
  Commonly used to store prepaid amounts of digital cash or personal information
  Smart card readers are built into or attached to a computer, door lock, vending machine, or other device
  Some smart cards store biometric data
  Use of mobile smart cards is an emerging trend

## Slide 39: Smart Cards

## Slide 40: Holographic Storage
Holographic storage
  Holographic drives connect to a computer via a serial attached SCSI (SAS) or Fibre Channel interface
  Uses multiple blue laser beams to store data in three dimensions
    Reference beam and signal beam
  Suited to applications in which large amounts of data need to be stored or retrieved quickly but rarely changed
    Archiving business data, medical records, TV shows,
sensor data , etc.

## Slide 41: Holographic Storage

## Slide 42: Storage Systems for Large Computer Systems
Business storage needs are growing exponentially
  Digital data produced is expected to double every two years through 2020
Storage server
  Hardware device containing multiple high-speed hard drives connected to the computer system or network
  Most are based on magnetic hard discs

## Slide 43: Storage Systems for Large Computer Systems

## Slide 44: Storage Systems for Large Computer Systems
RAID (redundant arrays of independent discs)
  Method of storing data on two or more hard drives that work together to do the job of a larger drive
  Mostly used to protect critical data on large storage systems
  Usually involves recording redundant copies of stored data
  Helps to increase fault tolerance

## Slide 45: Storage Systems for Large Computer Systems
Different levels of RAID:
  RAID 0 = disk striping (spread files over two or more hard drives)
  RAID 1 = disk mirroring (duplicate copy)
  Other level use a combination or striping and mirroring
Drobo system
  New RAID storage system
  Much easier to use than previous systems
  Offers continuous data redundancy

## Slide 46: Storage Systems for Large Computer Systems

## Slide 47: Magnetic Tape Systems
Magnetic Tape
  Plastic tape coated with a magnetizable substance that represents the bits and bytes of digital data
  Primarily used for backup and archival purposes
  Sequential access only
  Low cost per terabyte
  Most tapes today are in the form of cartridge tapes

## Slide 48: Evaluating Your Storage Alternatives
Product Characteristics to Consider:
  Speed
  Compatibility
  Storage capacity
  Convenience
  Portability
Most Users Require:
  Hard drive
  Recordable or rewritable optical drive
  Flash memory card reader
  USB ports

## Slide 49: Summary
Storage Devices:
  Magnetic Storage Devices
  Optical Storage Devices
  Solid State Storage Devices
  Data Read & Write Process.